## Slide 1
GINASHE DIGITAL ACADEMY · Cloud Launchpad
03
Networking
Fundamentals
Weeks 5–6 · 20 hours · NQF Level 4 · US 114076 · US 259604
7 App
6 Pres
5 Sess
4 Trans
3 Net
2 Data
1 Phys
GDA · Cloud Launchpad · Module 3 · Networking Fundamentals
1

## Slide 2
The OSI Model — 7 Layers
Every network communication passes through all 7 layers — the universal troubleshooting framework
7
Application
HTTP · HTTPS · FTP · SMTP · DNS · SSH
User opens browser → requests page
6
Presentation
SSL/TLS · JPEG · ASCII · MPEG
Encryption · Encoding · Compression
5
Session
NetBIOS · RPC · PPTP
Connection management
4
Transport
TCP · UDP — ports, reliability, flow
Segments · Port numbers
3
Network
IP · ICMP · ARP · Routing
Logical addressing · Path selection
2
Data Link
Ethernet · Wi-Fi 802.11 · MAC
Physical addressing · Frame delivery
1
Physical
Cat6 · Fibre · Wi-Fi radio · Copper
Bits on the wire
#
Layer
Key Protocols
SA / Cloud Context
GDA · Cloud Launchpad · Module 3 · Networking Fundamentals
2

## Slide 3
TCP vs UDP — Layer 4 Transport
The reliability vs speed trade-off that every cloud architect must understand
TCP — Connection-Oriented
SYN ─────────────→
← ─────────── SYN-ACK
ACK ─────────────→ [ connected ]
Every packet acknowledged — lost packets retransmitted
Ordered delivery guaranteed — arrives in sequence
Slower but reliable — every byte counted
Use for: SSH · HTTPS · Email · Database queries
SA example: Capitec balance check uses HTTPS/TCP
UDP — Connectionless
DATA ────────────→ (no reply needed)
DATA ────────────→ (lost? not retried)
DATA ────────────→ (order not guaranteed)
No handshake — data sent immediately
No acknowledgement — dropped packets stay dropped
Faster, lower latency, lower overhead
Use for: Live video · DNS · Gaming · IoT telemetry
SA example: DStv Now streaming uses UDP
GDA · Cloud Launchpad · Module 3 · Networking Fundamentals
3

## Slide 4
IP Addressing & CIDR Subnetting
Every VPC subnet you create requires a CIDR block — this calculation is on every cloud cert exam
CIDR
Subnet Mask
Usable Hosts
Common Cloud Use
/8
255.0.0.0
16,777,214
10.0.0.0/8 — Class A private (RFC 1918)
/16
255.255.0.0
65,534
Standard AWS VPC CIDR — most deployments
/24
255.255.255.0
254
One subnet per AZ — the standard design
/25
255.255.255.128
126
Split a /24 in half — two equal subnets
/26
255.255.255.192
62
Four subnets per /24 — smaller tiers
/27
255.255.255.224
30
DMZ or management subnet
/28
255.255.255.240
14
Bastion hosts, NAT gateway subnets
/30
255.255.255.252
2
Point-to-point link only
Formula: usable hosts = 2^(32−prefix) − 2 Example: /26 → 2^6 − 2 = 62 Network: 192.168.10.0 Broadcast: 192.168.10.63 Hosts: .1 – .62
GDA · Cloud Launchpad · Module 3 · Networking Fundamentals
4

## Slide 5
Security Groups & ufw Firewall
Lock down your server — allow only what is needed, deny everything else by default
ubuntu@ec2:~$
# Enable ufw — default deny incoming
$ sudo ufw enable
$ sudo ufw default deny incoming
$ sudo ufw default allow outgoing
# Allow only what is needed
$ sudo ufw allow from 41.x.x.x to any port 22
$ sudo ufw allow 80/tcp
$ sudo ufw allow 443/tcp
$ sudo ufw deny 8080/tcp
$ sudo ufw status verbose
Status: active
To Action From
22/tcp ALLOW IN 41.x.x.x
80/tcp ALLOW IN Anywhere
443/tcp ALLOW IN Anywhere
8080/tcp DENY IN Anywhere
SG Chaining Pattern
AWS Security Group best practice
Internet
0.0.0.0/0
Web SG
port 80/443 from 0.0.0.0/0
port 22 from mgmt IP only
DB SG
port 3306 from Web SG ID only
NOT from 0.0.0.0/0 !
GDA · Cloud Launchpad · Module 3 · Networking Fundamentals
5

## Slide 6
AWS VPC Architecture — af-south-1 Cape Town
Design this on paper before touching the console — the network your 2-tier app lives in
VPC 10.0.0.0/16
Internet Gateway
Internet
AZ: af-south-1a
Public subnet
10.0.1.0/24
EC2 web server
→ Route: 0.0.0.0/0 → IGW
Private subnet
10.0.11.0/24
RDS database
→ No internet route
AZ: af-south-1b
Public subnet
10.0.2.0/24
Load balancer (future)
→ Route: 0.0.0.0/0 → IGW
Private subnet
10.0.12.0/24
RDS standby (Multi-AZ)
→ No internet route
GDA · Cloud Launchpad · Module 3 · Networking Fundamentals
6

## Slide 7
VPC Troubleshooting — OSI Bottom-Up Method
5 issues cause 90% of connectivity failures — diagnose in this order every time
1
Missing SG Rule
Security group has no inbound rule for the port.
Check: EC2 → Security Groups → Inbound Rules
Fix: Add Allow rule for the required port and source
2
No IGW Attached
VPC has no Internet Gateway or it is detached.
Check: VPC console → Internet Gateways
Fix: Create IGW and attach it to your VPC
3
Route Table Wrong
Public subnet route table missing 0.0.0.0/0 → IGW.
Check: Subnet → Route Table → Routes
Fix: Add route 0.0.0.0/0 → your IGW ID
4
No Public IP
EC2 launched without auto-assign public IP.
Check: EC2 instance description → Public IPv4
Fix: Allocate Elastic IP and associate with instance
5
NACL Blocking
Network ACL has an explicit DENY rule (stateless!).
Check: Subnet → Network ACL → Inbound AND Outbound
Fix: NACL needs both inbound + outbound rules
OSI bottom-up checklist: L1 interface up? → L3 ping gateway? → L4 port open (telnet/nc)? → L7 app responding?
GDA · Cloud Launchpad · Module 3 · Networking Fundamentals
7

## Slide 8
Module 3
You built a cloud
network from scratch
Your VPC in AWS Cape Town is real infrastructure.
✓
Lab 3a
ping / traceroute from EC2
✓
Lab 3b
IP addressing and DNS
✓
Lab 3c
ufw firewall hardening
✓
Lab 3d
VPC build — paper design → console
Quiz: 20 questions · 70% pass
→ Next: Module 4 — Cloud Infrastructure
GDA · Cloud Launchpad · Module 3 · Networking Fundamentals
8